## Slide 1
Electric Vehicle Driving Range Prediction
Physics-Grounded Machine Learning Regression and Performance Benchmarking
Target Vehicle: 2013 Nissan Leaf (24 kWh Battery) | Reference: University of Michigan VED Schema

## Slide 2
BACKGROUND AND MOTIVATION
1. Introduction
Industry Context and Transition
- Global automotive shift toward Battery Electric Vehicles (BEVs) to achieve net-zero transport emissions.
- Range anxiety remains one of the primary deterrents to widespread consumer adoption.
- Unlike internal combustion vehicles with 500+ km range and 5-minute refueling, EVs require precise energy budgeting.
- A driver stranded due to unexpected range depletion creates safety, logistics, and roadside assistance challenges.
Limitations of Existing Systems
- Official Standard Ratings (WLTP / EPA): Tested under standardized laboratory temperature cycles; do not reflect highway or winter real-world driving.
- Dashboard In-Vehicle Estimators: Heavily rely on trailing moving averages of the last 10 to 50 km driven.
- Failure Under Volatile Conditions: Abrupt speed increases, cold snaps, or cabin heating cause sudden range drop-offs of 20% to 40%.
- Project Objective: Develop an adaptive machine learning model that maps multi-dimensional telemetry directly to continuous remaining range.

## Slide 3
TECHNICAL CHALLENGES
2. Problem Statement
Speed & Aerodynamic Drag
- Aerodynamic power loss scales with the cube of vehicle velocity (v^3).
- Driving at 110 km/h versus 50 km/h requires disproportionately higher power from the battery pack.
- Highway travel severely compresses driving range compared to urban regenerative cycles.
Sub-Zero Thermal Impact
- Li-ion electrolyte viscosity increases and internal resistance rises in cold weather (< 15 deg C).
- Available discharge capacity decreases up to 35% in freezing temperatures.
- Positive Temperature Coefficient (PTC) cabin heaters consume 1.0 to 4.5 kW directly from the traction pack.
- Unlike ICE cars, EVs have no waste engine heat to heat the cabin.
Mathematical Formulation
Goal: Construct a multivariate regression function f(X) -> Y.
Input Vector X in R^5:
1. Speed (km/h)
2. Ambient Temperature (deg C)
3. State of Charge (SoC %)
4. Road Slope (%)
5. Cabin HVAC Load (kW)
Target Output Y:
Continuous Remaining Range (km).

## Slide 4
EXISTING RESEARCH & METHODOLOGY COMPARISON
3. Literature Survey
Approach | Core Methodology | Key Advantages | Critical Limitations
Physics-Based Models | Mechanical differential equations (F_tractive = F_aero + F_roll + F_slope). | Rooted in physical principles; high transparency. | Requires complex calibration of drag area, friction, and mass; fails to generalize.
Statistical Moving Averages | Trailing window average of Wh/km over preceding 10-50 km. | Computationally trivial; easy to implement on low-cost ECUs. | Inherently reactive; introduces severe lag during speed or slope transitions.
Data-Driven Machine Learning | Supervised regression models trained on real vehicle telemetry (e.g., VED dataset). | Captures non-linear coupled interactions (HVAC + speed + cold); highly adaptive. | Requires empirical comparison to establish the optimal regression family (Trees vs. SVR).

## Slide 5
ARCHITECTURAL FRAMEWORK
4. Proposed Solution and Methodology
Step 1: Data Ingestion
Trip telemetry structured according to the University of Michigan Vehicle Energy Dataset (VED) schema.
Step 2: Preprocessing
Feature normalization through StandardScaler within an isolated scikit-learn Pipeline to prevent data leakage.
Step 3: Multi-Model Training
Comprehensive training of Random Forest, Gradient Boosting, and Support Vector Regressor (SVR).
Step 4: Benchmarking
Evaluation across MAE, RMSE, and R2 to determine the superior mathematical architecture.
Step 5: Model Deployment
Serialization of champion SVR model (.joblib) and integration with an interactive Streamlit UI.

## Slide 6
IMPLEMENTATION AND MODEL CONFIGURATION
5. Solution Development
Dataset & Physical Parameters
- Vehicle Profile: 2013 Nissan Leaf BEV (24 kWh nominal pack, 21.5 kWh usable capacity).
- Volume: 5,000 driving trip records spanning urban, suburban, and highway regimes.
- Split: 80% Training (4,000 samples) and 20% Unseen Testing (1,000 samples).
- Key Physics Encoded:
- Base consumption: 140 Wh/km at 50 km/h.
- Drag power penalty: ((Speed / 50)^1.8) * 35 Wh/km.
- Road slope resistance: Slope * 15 Wh/km.
- Auxiliary load: (HVAC kW * 1000) / Speed.
- Low-temp chemical degradation below 15 deg C.
Algorithms & Hyperparameters
Random Forest Regressor:
- 150 estimators, max depth: 12, min samples split: 4.
- Ensemble of de-correlated decision trees with bagging.
Gradient Boosting Regressor:
- 180 estimators, learning rate: 0.08, max depth: 5.
- Sequential boosting minimizing squared residual errors.
Support Vector Regressor (SVR):
- Radial Basis Function (RBF) non-linear kernel.
- Regularization parameter C: 100.0, Epsilon margin: 1.0.
- Coupled with StandardScaler in a scikit-learn Pipeline.
Deployment: Saved as models/svr_pipeline.joblib.

## Slide 7
EMPIRICAL EVALUATION ON 1,000 UNSEEN TEST TRIPS
6. Scalability & Performance Analysis
Model Architecture | MAE (km) | RMSE (km) | R2 Score | Outcome
Support Vector Regressor (SVR) | 1.30 km | 1.92 km | 0.9953 | Selected Champion
Gradient Boosting Regressor | 1.88 km | 2.69 km | 0.9909 | Evaluated Baseline
Random Forest Regressor | 2.52 km | 3.61 km | 0.9835 | Evaluated Baseline
Why SVR Outperformed Decision Trees
- Continuous Manifold: Battery consumption follows continuous physical differential curves (aerodynamic cubic drag, smooth thermal drop).
- Step-wise vs. Smooth: Decision trees use orthogonal axis-aligned cuts, producing piece-wise constant step approximations.
- RBF Kernel Advantage: Maps inputs to an infinite-dimensional Hilbert space, accurately fitting smooth non-linear curves.
Feature Importance & Sensitivity
1. State of Charge (SoC %): ~59% (primary energy reserve).
2. Ambient Temperature (deg C): ~15.5% (chemical impedance).
3. Vehicle Speed (km/h): ~10.5% (aerodynamic drag load).
4. Road Slope (%): ~8.2% (potential energy climbing load).
5. Cabin HVAC Load (kW): ~7.0% (parasitic traction pack draw).

## Slide 8
VISUAL VERIFICATION AND EDGE-CASE VALIDATION
6. Scalability & Performance Analysis
Real-World Edge Case Validation
Scenario A: Freezing Winter Highway
- Inputs: -5 deg C, 100 km/h, 80% SoC, 4.0 kW Heater
- Predicted Range: 39.8 km (62% range penalty)
Scenario B: Mild Spring City Commute
- Inputs: 20 deg C, 40 km/h, 80% SoC, HVAC Off
- Predicted Range: 106.3 km (Optimal operating zone)
Scenario C: Hot Summer Incline
- Inputs: 34 deg C, 60 km/h, 50% SoC, +4% Grade
- Predicted Range: 37.1 km
System Scalability Metrics
- Model Size: < 2 MB (embeddable on vehicle ECU).
- Inference Latency: < 2 milliseconds per sample.
- Deployment: Streamlit web dashboard + standalone CLI.

## Slide 9
SUMMARY AND FUTURE DIRECTIONS
7. Conclusion
Project Summary & Outcomes
- Successfully developed an end-to-end physics-grounded machine learning regression framework for EV driving range prediction.
- Evaluated three distinct model families on 1,000 unseen test trips; Support Vector Regression (SVR) demonstrated the highest precision (MAE: 1.30 km, R2: 0.9953).
- Demonstrated that ambient temperature and vehicle speed are the primary determinants of non-tractive energy loss.
- Successfully deployed the champion SVR pipeline into a real-time interactive Streamlit web dashboard and standalone CLI inference tool.
Future Scope & Enhancements
- Live In-Vehicle Telematics: Direct integration with OBD-II / CAN-bus hardware for real-time live-streaming range updates.
- Battery Degradation Modeling: Incorporate State of Health (SoH) and multi-year battery cell degradation tracking.
- Route-Ahead Navigation Integration: Interface with mapping and elevation APIs to predict range for planned future routes before departure.
- Driver Behavioral Profiling: Incorporate aggressive versus eco-driving habits into real-time dynamic range scaling.